## Slide 2: Employee Slips, Trips and Falls
U.S.:
25.3% of nonfatal workplace injuries are due to slips, trips and falls
14% of fatal workplace injuries are due to slips, trips and falls
The primary cause of lost workdays is slips and falls
MCIT:
Slips and falls account for 25% of reported workers’ compensation claims (both numbers and costs)
Members report 600 employee slip and fall injuries annually
These claims average $2 million annually
Notes: The National Safety Council provides the following definitions.
Slips: Where there is too little friction or traction between footwear and walking surface that cause sudden imbalance.
Trips: When a person’s foot collides (strikes, hits) an object causing the individual to lose his or her balance and fall.
[Run through the statistics]
Slip, trip and fall accidents can happen on walking surfaces in any season, but are more frequent in the winter due to ongoing icy and wet conditions. In the past several years, injuries due to slip and fall incidents are in the top five of the most frequently reported workers’ compensation claims made by MCIT member employees. Injuries can range from simple bruises to broken bones, dislocated joints and severe head and back injuries.
Given the prevalent number and significant costs of claims due to slips, trips and falls, all employees are encouraged to take simple steps every day to help reduce the chances of these types of accidents.

## Slide 3: Injuries Can Be Prevented
Weather-related hazards
Walking surface hazards
Stairs
Office hazards
Wet floors
Vehicles and equipment
Shop safety
Elevated work
Personal health
Notes: Today we will address major areas that contribute to slips, trips and falls and how to prevent such accidents:
Weather-related hazards
Walking surface hazards
Stairs
Office hazards
Wet floors
Entering and exiting vehicles and equipment
Shop safety
Elevated work
Personal health

## Slide 4: Weather
Hazards and Prevention
Notes: Minnesota has diverse weather: ice and snow in winter, frost and sleet in spring and fall, and rain in summer. Each of these weather-related variables represents a potential source for slips and falls. A number of sound strategies help reduce weather-related slips and falls. We will discuss four key components today.

## Slide 5: Proper Footwear
Choose footwear suitable to the weather conditions
Slip-resistant soles
Slip-on cleats or YakTrax™
Wear weather-appropriate shoes outside and change into dress/work shoes once in the workplace
Notes: The first is proper footwear. Footwear suitable to weather is a key factor in preventing slip and fall accidents. Properly selected footwear can significantly increase the traction in a given situation and decrease slip potential. Employees are encouraged to wear suitable footwear for the conditions, such as:
Boots or shoes with slip-resistant soles.
Slip-on cleats or YakTrax. They provide extra traction in ice and snow.
A good practice is to wear weather-appropriate shoes outside and change into dress or work shoes once in the workplace.

## Slide 6: Free Hands
Carry materials in shoulder bags or carts
Keep a clear view of the path ahead
Notes: When navigating sidewalks, parking lots or stairs in slick conditions, it is important to keep hands as free as possible to help maintain balance and hold rails:
Carry materials in shoulder bags or carts
Keep a clear view of the path ahead

## Slide 7: Take Your Time
Allow adequate travel time
Better to be late than not to get there at all due to an injury
Notes: A major factor in causing weather-related slips and falls is walking too fast for the conditions. Even with proper footwear, rushing can cause falls:
Allow adequate travel time
Better to be late than not to get there at all due to an injury

## Slide 8: Maintenance
Report hazards to maintenance manager/appropriate person:
Slick areas
Accumulated snow or water
Wet floors
Saturated rugs
Notes: When employees find hazards, they are encourage to immediately report them to the maintenance manager or appropriate person. Common hazards employees encounter are:
Slick areas indoors and outdoors
Accumulated snow or water
Wet floors
Saturated rugs

## Slide 9: Walking Surfaces
Hazards and Prevention
Notes: People typically slip, trip and fall because the walkway conditions they encounter are different from what they expect. Therefore, small defects in the walking surface can become a big nuisance.

## Slide 10: Changes in Elevation
Common hazards:
Heaved sidewalks or other pavement
Potholes
Cracked pavement
Cracked or missing tiles
Control hazards:
Mark hazards
Temporarily close walkway
Barricade area
Repair as soon as possible
Notes: Abrupt changes in elevation can catch toes and cause falls.
Common hazards are:
Heaved sidewalks or other pavement
Potholes
Cracked pavement
Cracked or missing tiles
There are a number of ways to manage these hazards. Choose the best method for the situation:
Mark hazards
Temporarily close walkway
Barricade area
Repair as soon as possible

## Slide 11: Camouflaged Hazard
Blue parking curb blends into the painted parking space
This contrasting parking curb is easily noticed
Notes: Sometimes hazards are almost impossible to see because they are camouflaged. Be on the lookout for these types of problems so you can avoid them, but also so you can report them to the appropriate person.

## Slide 12: Steps Blend in to Floor
Before
After
Notes: The steps visually blend into the floor, making it difficult for people to recognize that they are coming upon a set of steps. The added handrails provide a visual cue to the change in elevation.

## Slide 13: Stairs
Hazards and Prevention
Notes: The basic task of climbing and descending stairs accounts for numerous falls each year that result in injury.

## Slide 14: Using Stairs Safely
Carrying large loads can make it difficult to see steps, increasing the chance of falling
Slow down going up and down stairs
Ensure good footing on each step
Use railings to help maintain balance
Keep eyes on the path
Do not carry items that obstruct the view of steps
Notes: The primary cause of stairwell slips and falls is the loss of balance. To help maintain your balance and prevent falls on steps:
Slow down going up and down stairs
Ensure good footing on each step
Use railings to help maintain balance
Keep eyes on the path
Do not carry items that obstruct the view of steps

## Slide 15: Stair Maintenance
Keep stairs clear of clutter. Items on steps can become a tripping hazard.
Replace worn traction tape as it wears out
Notes: Proper maintenance of stairs is also important for slip and fall prevention. Employees are encouraged to remedy hazards they see, such as removing clutter, or to report hazards they cannot fix, such as worn traction tape, loose hand rails or accumulating snow.

## Slide 16: Office
Hazards and Prevention
Notes: In office settings, some of the more common contributing factors to slip and fall accidents are unsecured carpeting, curled rugs, cords strewn in walkways and under desks, and drawers left open.

## Slide 17: Recognize Hazards, Take Action
Common Hazards/Unsafe Behaviors | Smart Choices
Power cords that cross pathways or dangle under desks | Secure power cords out of the way to avoid crossing walkways or dangling from desks. Cover cords with a bridge when they must cross pathways.
Wrinkled, curled or uneven rugs | Flatten rugs. Inform maintenance staff of the problem as needed.
Transitions from one type of surface to another (e.g., carpet to tile) | Be alert to changes in surface types and watch where you place your feet.
Open drawers | Close drawers as soon as you are done using them.
Notes: Employees should keep eyes on the path ahead and look for potential hazards and are encouraged to report hazards that they cannot remedy themselves.
[Review table]

## Slide 18: Wet floors
Hazards and Prevention
Notes: One element that contributes significantly to reduced traction is the presence of moisture on floors. Wet floors can occur in office buildings, shops, nursing homes, kitchens and any other location with impermeable flooring such as tile, cement and marble.

## Slide 19: Wet Floors in the Workplace
Leaking roof or plumbing
Melting snow or ice carried in by footwear
Housekeeping duties such as mopping or washing
Spilling of employees’ drinks and lunches
Splashing from sinks and drinking fountains
Notes: Several causes of wet floors in the workplace are:
Leaking roof or plumbing
Melting snow or ice carried in by footwear
Housekeeping duties such as mopping or washing
Spilling of employees’ drinks and lunches
Splashing from sinks and drinking fountains

## Slide 20: Reduce, Eliminate Wet Floors
Immediately mop up excess moisture or spills
Place warning signs in walkways when floors are wet
Fix leaks immediately
Place carpets at building entrances and change them as they become saturated
Use slip-resistant mats in front of sinks, dishwashers, washing machines
Take time when walking in areas that are generally wet
Take corrective action immediately or report problems when found
Notes: To reduce or eliminate moisture in walkways, practice these commonsense strategies:
Immediately mop up excess moisture or spills
Place warning signs in walkways when floors are wet
Fix leaks immediately
Place carpets at building entrances and change them as they become saturated
Use slip-resistant mats in front of sinks, dishwashers, washing machines
Take time when walking in areas that are generally wet
Take corrective action immediately or report problems when found

## Slide 21: Vehicles and Equipment
Hazards and Prevention
Notes: Many people sustain serious injuries from slips and falls while attempting the simple task of getting into or out of cars or large equipment vehicles.

## Slide 22: Maintain 3 Points of Contact
Keep two hands and one foot or two feet and one hand on the vehicle until safely on the ground or in the vehicle.
Notes: The best means of preventing slips and falls from equipment and passenger vehicles is to use three points of contact when mounting and dismounting. This process means that either two hands and one foot or one hand and two feet are in contact with the equipment.
To ensure proper mounting and dismounting procedures for large equipment, employees should consult with the manufacturer’s recommended procedure. In many cases, manufacturers may provide training videos on the recommended procedures.

## Slide 23: More Safety Measures
Only climb on or get off when the equipment or vehicle is fully stopped
Always face the truck or equipment when getting in or out of it
Ensure that the points of contact are clear of debris and mud
Descend equipment slowly
Only use points of contact that were intended for climbing onto or off of the vehicle
Do not climb on or get down while carrying an item. Put the item on the vehicle’s floor
Never jump from equipment
Be aware of the surface onto which you are stepping
Notes: Additional tips for safely getting into and out of vehicles:
Only climb on or get off when the equipment or vehicle is fully stopped.
Always face the truck or equipment when getting in or out of it.
Ensure that the points of contact are clear of debris and mud.
Descend equipment slowly.
Only use points of contact that were intended for climbing onto or off of the vehicle. Hubs and such are not meant to be used for climbing on or off of equipment.
Do not climb on or get down while carrying an item. Put the item on the vehicle’s floor.
Never jump from equipment. If an employee jumps from equipment, he or she may land off balance or on an uneven surface and fall, suffering an injury.
Be aware of the surface onto which you are stepping: Sand and oily spots in parking lots can lead to slips and falls just like snow and ice.

## Slide 24: Maintenance Shops
Hazards and Prevention
Notes: Maintenance shops are multi-operational sites that harbor the potential for numerous slip and fall exposures due to the equipment and materials used, and the byproducts of the work.

## Slide 25: Recognize Hazards, Take Action
Common Hazard | Recommended Prevention Strategy
Cords and hoses left on shop floor | Store hoses and cords on retractable reels. Best if reels extend from the ceiling.
Accumulation of wood and metal shavings and dirt | Sweep floors regularly
Oil spots from mechanical work | Clean up oil immediately
Equipment or tools left in walkways | Store equipment and materials in a manner that allows space for walkways.
Boards or metal strips that extend into walkway | Remove boards and metal strips that extend into walkways.
Poor lighting | Replace light bulbs, add more light fixtures
Uneven surfaces or protrusions due to drains, lift rails and thresholds | Mark uneven surfaces or protrusions on floor with bright paint
Notes: [Review table]

## Slide 26: Elevated work
Hazards and Prevention
Notes: Slips and falls from elevated work platforms such as ladders, scaffolds and decks are not as frequent as other types of slips and falls, but the resulting injuries to employees tend to be serious.

## Slide 27: Ladder and Stepstool Safety
Causes of falls from ladders:
Using a ladder that is too short for the task
Setting up ladder incorrectly or in an unstable manner
Overreaching
Climbing/descending with a load in hand
Employees should:
Use correct ladder for task (height, weight limits, type)
Inspect ladder prior to use
Correctly set up ladder, secure it if necessary
Climb/descend using three points of contact
Notes: Common causes of falls from ladders are:
Using a ladder that is too short for the task
Setting up ladder incorrectly or in an unstable manner
Overreaching
Climbing/descending with a load in hand
To help prevent falls from a ladder or stepstool:
Use correct ladder for task (height, weight limits, type)
Inspect ladder prior to use
Correctly set up ladder, secure it if necessary
Climb/descend using three points of contact

## Slide 28: Do Not Use Makeshift Platforms
Chairs or other makeshift platforms are not intended for or safe for elevated work
Notes: Chairs or other makeshift platforms are not intended for or safe for elevated work. Never use them to reach items or work overhead.

## Slide 29: Scaffolding Safety
All OSHA standards (1910.28) should be followed at all times
Only qualified employees should set up scaffolding
Inspect scaffolding daily to ensure all rails are in place and properly secured
Climb scaffolding using three points of contact
Notes: Poor construction or lack of proper railings are two of the most common reasons people fall from scaffolding. Safe and proper use of scaffolding can significantly reduce the potential for falls. Follow these steps when using scaffolding:
Adhere to all OSHA standards at all times
Only qualified employees should set up scaffolding
Inspect scaffolding daily to ensure all rails are in place and properly secured
Climb scaffolding using three points of contact

## Slide 30: Elevated Platform Safety
Use basket trucks or lifts with proper fall protection
Never use the bucket of a loader as a work platform
Always ensure that the railing system of elevated decks are in place, and any gates or chains are in place before starting a task
Notes: For moving work platforms:
Use basket trucks or lifts with proper fall protection.
Never use the bucket of a loader as a work platform. Buckets are not designed for this task. Many serious injuries occur when employees are knocked out of the bucket.
For elevated decks:
Always ensure that the railing system is in place, and any gates or chains are in place before starting a task.

## Slide 31: Personal health
Hazards and Prevention
Notes: Ice and snow, uneven walking surfaces and other contributing factors are generally the main causes of slips, trips and falls. However, certain personal health issues can also contribute to slip, trip and fall accidents.

## Slide 32: Common Contributing Factors
Chronic health conditions that cause limited mobility, flexibility or balance can be a factor
Low blood sugar can cause disorientation, loss of balance or fainting
Medications can affect basic motor skills and cause imbalance
Sleep deprivation can affect balance similar to some medications
Notes: Be aware of how your personal health could contribute to potential for slip, trip and fall accidents.
Common health issues that contribute to accidents:
Chronic health conditions that cause limited mobility, flexibility or balance can factor into slips, trips and falls.
Low blood sugar can make a person disoriented, lose his or her balance or faint.
Medications, such as cold medicines, cough syrup and some prescriptions, can affect basic motor skills and cause imbalance. Employees taking medications that can affect their performance are encouraged to report this to their supervisors.
Sleep deprivation can affect balance in a manner similar to some medications. Balance and awareness can be impeded if a person is tired.

## Slide 33: Discussion
Ask Questions and Share Experiences